## Slide 1
The Chemical Engineering Problem
BEYOND BLACK BOX ML: RECOVERING GOVERNING EQUATIONS TO PREDICT SERIES PARALLEL REACTOR YIELD
Fugacity 2026
ML Hackathon
TEAM NAME : OUTLIERS
TEAM MEMBERS: ASHISH (24CY10012)
INDIAN INSTITUTE OF TECHNOLOGY KHARAGPUR

## Slide 2
Build a predictive data driven surrogate model to instantly and accurately forecast the overall yield percentage of Product B at the reactor exit.
Bridging chemical engineering and computer science to give process engineers a tool for instant, real time operating setpoint adjustments
Industrial Impact
The kinetic and thermodynamic behaviors of the reactions create complex, non linear trade offs between flow rates, inlet concentrations, and thermal profiles.
System Complexity
Modern chemical facilities rely on complex computational fluid dynamics and boundary value problem (BVP) simulations. While rigorous, these are too computationally expensive and slow for real time plant optimization.
The Computational Bottleneck
The process utilizes a continuous flow, non isothermal reactor involving a highly sensitive series parallel reaction network
The Physical System
Problem & Industrial Relevance
The Objective
Dataset : 150 train / 50 test
Metric : RMSE

## Slide 3
Chemical & Process Understanding
Kinetic Tradeoff
Thermally Self Destabilizing Flow
The Jacket Only Fallacy
Residence Time Dynamics
Validating "ZeroYield" Data
The side reaction (B → C) is significantly more temperaturesensitive than the desired reaction (A → B). Consequently, raising the temperature destroys Product B faster than it synthesizes it.
  The primary reaction A → B is endothermic (β₁ < 0), causing the feed to selfcool upon entry.
  The secondary reaction B → C is exothermic (β₂ > 0), releasing heat downstream exactly where Product B concentration peaks and is most vulnerable to degradation.
E₂ ≫ E₁
Goal Setting
Models utilizing only a jacket energy balance fail because they are forced to reproduce a sharp thermal switch with a single Arrhenius term. This results in a physically impossible activation energy of E₂ ≈ 634 kJ/mol. Incorporating both reaction enthalpies successfully resolves this.
Strategy Design
The yield versus τ (where τ = L/Q) exhibits an interior maximum. This optimum shifts to shorter residence times (τ) as the mixture temperature (T_mix) rises.
Preparation
The 37 exact zeroyield rows are not sensor failures or missing data. They represent a physical selectivity cliff past 460 K where Product B is completely consumed into Byproduct C.
Execution Stage
First Order Kinetics Supported
Yield is independent of inlet concentration (r = 0.009), consistent with first order. Freeing the order worsens CV, so we keep n = 1.

## Slide 4
ML Methodology & Approach
01
04
02
05
03
06
Recovered the exact differential equations for energy and mole balances instead of relying on black box ML
GOVERNING EQUATIONS
Deployed an unconditionally stable ETD midpoint integrator to accurately handle sharp thermal switches in the reactor.
STABLE INTEGRATION
Executed strict 5-fold crossvalidation alongside 24 wide multistart restarts to secure the true global optimum.
CROSS
VALIDATION
Trained an ExtraTrees regressor solely on physics residuals, using a deliberate shrinkage weight to prevent overfitting
ML RESIDUALS
Inferred data contamination to justify using a Cauchy loss function for highly robust parameter optimization
ROBUST FITTING
Combined the dominant physical model with the minor ML correction to generate the highly accurate final prediction.
HYBRID PREDICTION

## Slide 5
Results & Model Performance
01
02
03
04
Pure ExtraTrees scores 18.09 RMSE; the 5parameter physics model, with no ML, scores 10.76.
Physics Outperforms ML
Every performance gain came from adding a physical term, never from adding model capacity.
The Ablation Ladder
Modelling both reaction enthalpies dropped apparent E₂ from 634 to 242 kJ/mol impossible to defensible.
Corrected Kinetics
The 5 parameter physics beats ML by 3.6× on trimmed RMSE. ML enters only as a shrunk correction.
Why λ = 0.3
05
06
07
08
β₁ = −40.8 K, β₂ = +37.4 K: the feed selfcools, then the side reaction reheats downstream.
Opposing thermal effects
5-fold CV repeated over seeds, with the physics refit inside every fold.
Leak free validation
Reproduces the interior optimum in τ shifting shorter with temperature, and the 37 zeroyield runs.
Physically consistent
λ is weakly identified and tuned on the scoring CV; E₂ stays apparent, not mechanistic.
Stated limitations
Leaderboard RMSE: 11.2

## Slide 6
Failure Analysis & Limitations
01
02
03
04
Operating near the cliff
Feed or flow change
Above ~460 K yield collapses steeply; small temperature errors become large prediction errors
Inerts, cofeeds, or laminar flow break the firstorder and idealplugflow assumptions.
Jacket fouling
Heat transfer h degrades, shifting the thermal switch and moving the optimal residence time.
Catalyst deactivation
Activity k₁ falls over time; the model assumes it constant and overpredicts yield.
05
06
07
08
Unmodelled parallel path
Diagnosing the source
The brief calls the network series-parallel; we modelled A→B→C. A genuine A→C route would show as a systematic offset.
Refit online and see which constant moves: h means fouling, k₁ means deactivation, offset means sensors.
Weakly identified parameters
Reaction order's interval is [0.87, 1.91]; a residual correlation with Q·C₀ survives at r ≈ 0.22.
Extrapolation limits
Physics stays valid outside the training box; the tree residual term flattens and misleads.
Thank You!!
Team Name : Outliers